## Slide 1
Progress Towards Developing
Single Trapped Ion Optical Atomic Clock
Subhadeep De
CSIR-National Physical Laboratory, New Delhi
QIPA-2018, 02-08 December 2018, HRI, Allahabad

## Slide 2
CSIR-NPL is the National Metrology Institute in India
It has the mandate of
establishing and maintaining the SI standards through the Act of Parliament
“Standard” follows an unbroken chain of tractability to the SI unit
SI definition
International realization
National realization

## Slide 3
Navigation
Let us start with

## Slide 4
Position
P1
t1
Transmitter sends the signal at time ts with a “time stamp” on it
Receiver receives the signal at time te with another “time stamp” on it
- Transmitter and receiver “clocks are synchronized”
Distance between transmitter and the receiver is calculated as d1 = c × (te – ts)
  velocity of light “c” is a constant
Transmitter - I
Receiver
d1 km

## Slide 5
d1 km
Position
P1
t1
d2 km
t2
Position
P2
Transmitter - I
Receiver
Transmitter - II

## Slide 6
t1
t2
t3
Position
P1
Position
P2
Position
P3
Accuracy of 1 meter requires to synchronize clocks within
1/c ~ 3 ns precision
Transmitter - I
Receiver
Transmitter - II
Transmitter III
d1 km
d2 km
d3 km

## Slide 7
t1
t2
t3
Position
P1
Position
P2
Position
P3
Transmitter - I
Receiver
Transmitter - II
Transmitter III
d1 km
d2 km
d3 km

## Slide 8
Accurate “time stamping” to the transmitter & receiver and “time synchronization” between them with respect to a common stable reference is required for the correlation measurement.
High attenuation due to the free space transmission and low detector efficiency requires longer integration to get the desired S/N.
At the receiver: Average detection rate
From the transmitter: pulse train of laser light
Time
Counts [s-1]
Correlated photons
Transmission & Detection in
Long Distance (Free Space) Quantum Communication
Time
Example: 1.2-km-long free-space transmission
F. Steinlechner et. al. Nat. Comm. 8, 15971 (2017)

## Slide 9
With efficient & fast detectors  low integration time
Allowed pulse rate from the transmitter will be limited by the Time stamping / Time synchronization accuracies
Time [s]
Time [s]
Counts [s-1]
Timing accuracy
Search range
Pulse rates can be faster
with more accurate timing devices
Correlated photons
Time [s]

## Slide 10
Excitation
|g
|e

Principle of the Atomic Clocks
de-excitation
fluorescence
detection
SERVOed to
stabilize at
oscillations
Fine
structure
4
3
Hyperfine
structure
9 192 631 770 Hz
6S1/2
1s is the duration for
Caesium
in SI unit
Accuracy: beam clock 10-14 & fountain 10-16
SI definition may change in 2026 to an optical transition

## Slide 11
Allan Deviation =
Quality factor
Theoretical
Number of species, N
Statistical
Number of measurements,
τ is total measurement time
T duration for each measurement
Signal-to-noise-1
Signal = number of events
Noise = (number of events)1/2
Ref: http://tf.nist.gov/general/glossary.htm
Accuracy of an Atomic Clock

## Slide 12
10-18
210-18 : Sr-atom
Ushijima et. al.,
Nature Photonics 9, 185 (2015)
Cs-fountain-I
CSIR-NPL
Cs-fountain
NPL-UK
310-18 : Yb-ion
N. Huntemann et. al.,
Phys. Rev. Lett. 116, 063001 (2016)
1.410-18 : Yb-atom
W. F. McGrew et. al., Nature (2018)

## Slide 13
Single Trapped Ion Optical- Standard

## Slide 14
199Hg+
S. A. Diddams, et. al., Science 293, 825 (2001).
171Yb+
N. Huntemann, et. al., PRL 108, 090801 (2012).
88Sr+
H. S. Margolis, et. al., Science 306, 1355 (2004).
Ion | λ [nm] | Transition | Laboratories
223Ra+ | 828 | 2S1/2 – 2D3/2 (E2) | KVI Netherlands
199Hg+ | 282 | 2S1/2 – 2D5/2 (E2) | NIST USA
171Yb+ | 435 | 2S1/2 – 2D3/2 (E2) | PTB Germany
171Yb+ | 467 | 2S1/2 – 2F5/2 (E3) | NPL UK, PTB Germany,
115In+ | 236 | 2S0 – 3P0 (HIT) | MPQ Germany, U. Washington
88Sr+ | 674 | 2S1/2 – 2D5/2 (E2) | NPL UK, NRC Canada
43Ca+ | 729 | 2S1/2 – 2D5/2 (E2) | Uibk Innsbruck, CRL Japan, CAS China
27Al+ | 267 | 1S0 – 3P0 (HIT) | NIST USA, VU Netherlands
167 nm
267 nm (HIT)
Δνnat=0.5 mHz
27Al+
T. Rosenband, et. al., PRL 98, 220801 (2007).
CSIR-NPL
World wide Trapped Ion Optical Frequency Standards
Why Ytterbium ?
CIPM has endorsed the 6s 2S1/2(F=0, mF=0) – 4f136s2 2F7/2(F=3, mF=0) transition as a secondary frequency standards.
First order Zeeman insensitive clock transitions.
Off the shelve lasers.
Yb+ chemically reacts with residual H2 and produces hydride, which photodissociates to Yb+ in the presence of cooling laser and that gets retrapped.
Potential candidate for probing fundament science: violation of the local Lorentz symmetry, temporal constancy of the fundamental constant.

## Slide 15
Table is adapted from - H. S. Margolis, Contemporary phys. 51, 37 (2010).
Sensitivity
time
Sr-atom
Yb+
Inter-comparison of Yb+ with Sr optical clocks
Is it really a constant?
NO !
Comparing Hg+ & Al+ transitions
Ref. T. Rosenband,et. al., Science 319, 1808 (2009) .
Fundamental Physics: 10-19 s or better clock accuracy is required
year -1
Probing Temporal Constancy of
Fundamental Constants

## Slide 16
ISS
satellite
Master clock
On board clock
clock 1
clock 2
Energy level shift of the state:
Local position invariance (LPI)
Local Lorenz invariance (LLI)
Estimated sensitivity of LLI-violation
Table is adapted from – V. A. Dzuba, et. al., Nature Phys. doi: 10.1038/nphys3610 (2016).
R. Bluhm, et. al., Phys. Rev. Lett. 88, 090801 (2002)
Probing the Local Lorenz Invariance (LLI) violation with Yb-ion

## Slide 17
cooling & detection
optical pumping
hyperfine repump
369.5 nm
repump 1
935.2 nm
467 nm (E3-octupole)
repump 2
760 nm (quadrupole)
4f146s 2S1/2
4f146p 2P1/2
4f145d 2D3/2
4f135d6s 3D[3/2]1/2
6s24f13 2F7/2
|1
|0
|1
|0
|0
|1
|2
|1
|4
|3
|2
|1
4f135d6s 1D[3/2]3/2
Energy levels of 171Yb+
Electrodynamic (Paul) Trap
4f146s2 1S0
4f146s6p 1P1
Continuum
399 nm
369.5 nm
atom  ion
Single Trapped ion Optical- Standards

## Slide 18
Cooling cycle: 369.5 nm, 760 nm & 935 nm
Helmholtz coil
& Stable
current source
Characterization of trap
Ion Trap: designed, in Fabrication stage
UHV: Chamber designed & Fabricated
Atomic Oven: designed, in testing stage
RF Resonator:
Ready to use
AOM & EOM drivers: in testing stage
Automated Control & Acquisition: developing
Imaging & Detection of single ion
Frequency Stabilization
Frequency Comb for inter-comparison
Ultra Stable narrow
linewidth Clock @ 467 nm
Compensation electrodes design & fabrication
Systematic shifts cancellation
Optics design & fabrication: Partly done
Computer controlled DC power supply
Trapping ions and studying dynamics
Building blocks require indigenous development of the instruments

## Slide 19
1
2
3
Drawbacks:
More degrees of rotations due to multiple fitting screws
Mutual misalignment
Tight fitting of the electrodes at desired precision failed always
Bulky Macor insulator
Blocking of the lights due to overall bulky structure
Drawbacks:
Relative misalignment resulting from single screw assembly
Difficult assemble the electrodes by tight fitting
Advantages:
NO obstruction of lights coming at the desired angles
NO relative rotation
Easy electrode assembly
TWO legs for mounting with the feedthrough gives better stability
Mounting hole for Pt100
‘Design of the Ion Trap and Vacuum System for 171Yb-ion Optical Frequency Standard’- A. Rastogi et. al., MAPAN-J. Metrol. Soc. India 30, 169 (2015).

## Slide 20
Trap Geometry has influence on
Nature of the confining potential
(desired is quadrupole)
Trajectory of the ions
(micromotions)
Systematic uncertainty
(Electric quadupole shift)

## Slide 21
Identifying The Suitable Trap Geometry
Anharmonicity | Schrama (1993) | Beaty (1986) | Beaty (1986) | Stein (2010) | NPL India
¦a40 / a20¦ | 0.004975 | 0.00232 | 0.003529 | 0.01365 | 0.0024
¦a60 / a20¦ | 0.088382 | 0.00014 | 0.000816 | 0.00505 | 0.0092
¦a80 / a20¦ | 0.0065468 | 0.013859 | 0.00132 | 0 | 0.0042
¦a10 0 / a20¦ | --- | --- | --- | --- | 0.0023

## Slide 22
x
y
z
x
y
z
Trajectory
Motion of ion in the potential
Micromotions - not curable by laser cooling
Micromotion measurement in- D. J. Berkeland, et. al., J. App. Phys. 83, 5025 (1998).
J. Keller, et. al., arXiv:1505.05907v1 (2015).

## Slide 23
2ro = 1 mm,
θi = 10o,
θo = 45o
2ro = 0.5 mm,
θi = 0o,
θo = 45o
2ro = 1 mm,
θi = 11o,
θo = 45o
2zo = 0.6 mm,
θi = 0o,
θo = 45o
2ro = 1 mm,
2zo = 0.6 mm,
2ro
2zo
θi
θo

## Slide 25
rf
C
Helical resonator
B
Connector
A
Trap

## Slide 26
UHV Chamber
Trap
Loads Resulting from the Trap
R’1
R3
R4
R’4
R5
R1
R6
R’6
R’5
C1
C2
C’5
C5
C8
C7
C9
R2
C3
C’3
C4
C6
C’6
R7
R’7
Ri and Ci indicate resistances and capacitances:
Estimated analytically and through numerical analysis (COMSOL Multiphysics)

## Slide 27
Variation of resonance frequency and quality factor
Extra
Micromotions
Effect of the Loads Resulting from the Trap
CT
CR
RE
CR

## Slide 28
Thermal image showing temperature increase at UAC = 1 kV, ωrf = 2π x 15.4 MHz. In-ion heats up by 1.0 K resulting to BBR shift of 2 x 10-19
(J. Keller et. al.)
Skin depth
AC current
Energy transfer
Heating of the material due to energy dissipation
AC flowing through a conductor
References:
[1] Doležal, M. et al., Metrologia 52, 842 (2015).
[2] Keller, J. et al., J. Phys. Conf. Ser. 723, 012027 (2016).
[3] Zhang, P. et al., J. Appl. Phys. B 50, 015002 (2016).
Absorption of the RF and resulting heating of the Ion-trap
1.72 K temperature increase of Ca-ion results to BBR shift of 5.4 x 10-18 (P. Zang et. al.)

## Slide 29
Equal path lengths on both sides
AC
t
t
AC
Equal path lengths on both sides
t
t
Heating of the Ion-trap Due to Phase Difference in RF
Relative phase shift results to
Potential difference Vo
Analogous to a Capacitor
Vo
Phase difference of the RF at opposite ends
Resulting current flow
Increase of temperature
Total resistance of the RF path
D. J. Berkeland et. al., J. Appl. Phys. 83, 503 (1998)

## Slide 30
Loads Resulting from the Trap
R1
R1’
R2
R3
R4
R5
R6
R5’
R6 ’
C1
C2
C3’
C3
C4
C5
C5’
C6
C6’
C7
C8
C9
R4’
R7
R7’
C8’

## Slide 31
(a) resonant frequency and (b) quality factor with capacitance for the resonator itself and for the resonator + connector without the ion-trap. The experimental data (black) and the measured capacitance (blue).
(a) Excess capacitance (Cex) phase di- erence and (b) the BBR shift at RF amplitudes 250 V, 500 V, 750 V and 1000 V resulting from the machining inaccuracy are shown.
Lakhi Sharma et. al., Sci. Reports 8, 16884 (2018).
At 1 kV, 15 MHz RF and with ±10µm machining inaccuracy will result to ±0.42 K heating of the trap. This results to 43 mHz shift for the Yb ion E3-clock transition that corresponds to fractional frequency
un-certainty 6.6x10-17
due to the BBR effect.

## Slide 32
Indigenously Developed Electronics
DC Power supply
Photodiode amplifier and readout
Camera multiplexor
All-digital locking electronics
Data acquisition system
Computer controlled dc voltage source
AOM/ EOM drivers
Shutter drivers
Computer controlled current source
1. N. Batra, et. al., IEEE Conf. Proc of 2nd International conference on control, instrumentation, energy and communication, Kolkata, 78 (2016). Doi: 10.1109/CIEC.2016.7513823.
2. A. Acharya et. al, Measurements 61, 16 (2015).
3. A. Roy et. al., Metrology Soc. of India Mapan (2017)

## Slide 33
Lock-in amplifier
PID Servo Controller
Function Generator
Oscilloscope
FPGA
PID SERVO and Lock-in
Digital control and software implementation for
Synthesizer
Filters
Phase sensitive detection
PID
Salient features
Compact
Less insensitive to noise pickup
Computer controlled
Low cost

## Slide 34
2.0
1.5
1.0
0.5
0.0
-0.5
0.30
0.35
0.40
0.45
0.50
0.55
0.60
0.65
Voltage ( × 100 mV )
Time (ms)
0.9
0.8
0.7
0.6
0.5
0.4
Wavelength change (pm)
20
24
18
22
Temperature (C)
10:30
14:30
18:30
22:30
02:30
06:30
10:30
Day 1
Day 2
Time
Laser frequency stabilization at CSIR-NPL
PD voltage
Piezo voltage
Error signal
Wavelength meter reading

## Slide 35
2.0
1.5
1.0
0.5
0.0
-0.5
0.30
0.35
0.40
0.45
0.50
0.55
0.60
0.65
Voltage ( × 100 mV )
Time (ms)
0.9
0.8
0.7
0.6
0.5
0.4
Wavelength change (pm)
20
24
18
22
Temperature (C)
10:30
14:30
18:30
22:30
02:30
06:30
10:30
Day 1
Day 2
Time
Laser frequency stabilization at CSIR-NPL
Low coherence optical interferometry
at BARC Vizag
Auger electron spectroscopy at CSIR-NPL

## Slide 36
(1) Sci. Reports 8, 16884 (2018).
(2) J. Phys. B:At. Mol. Opt. Phys. 50 205201 (2017).
(3) Mapan-J. Metrol. Soc. India, DOI 10.1007/s12647-017-0241-5 (2017).
(4) MAPAN-J. Metrol. Soc. India, DOI 10.1007/s12647-017-0209-5 (2017).
(5) Chin. Phys. B 25, 113703 (2016).
(6) IEEE Conf. Proc of 2nd International conference on control, instrumentation, energy and communication (2016).
(7) MAPAN-J. Metrol. Soc. India 30, 169 (2015).
(8) Rev. Sci. Instrum. 86, 056104 (2015).
(9) arXiv:1405.5399 (2015).
(10) Int. J. Mod. Phys. B 29, 1550051 (2015).
(11) Measurements 61 16 (2015).
(12) Current Science 106 1348 (2014).
(13) Appl. Phys. B: lasers and optics 114 527 (2014).
In the planning phase
Conclusion
RF resonator
Lasers and optics
Necessary electronics
Ion trap design
Ultra high Vacuum
Ytterbium oven
Frequency stabilization
Ultra stable cavity
Frequency comb
Imaging/ detection
Automation/control system
Generation of UTC(NPLI)
GPS link with BIPM
TWSTFT with NIMs
Production of
ions
Ion trapping
Laser cooling
Probing the clock transition
Time keeping
Trapping and laser cooling
Work is in progress
already exist at CSIR-NPL

## Slide 37: T
Atish Roy
Subhasis Panja
Lakhi Sharma
Harish
Rathor
Kavita Kumari
Neelam
Sankar Majhi
Anindya Rastogi
Sathi Chakraborty
Amitava Sengupta
Collaborators:
Aranya Bhattachariya, JNU
Bindiya Arora, GNDU
Bijoy K Sahoo, PRL
S R Mishra, RRCAT
Jeroen Koelmeij, VU
H
A
N
S
Present members
Former members
Funds:
Single Trapped ion Optical- Standard
V N Ojha
K
Neha Batra